## Slide 1
PSXM Steering Magnet Design
Two-Week Progress Report - 2026-07-28 to 2026-08-12
Jintian Wang
Group meeting (Node 5) - 2026-08-12

## Slide 2
Overview - What Was Done in the Last Two Weeks
Week 1 (7/28-8/3): Node 3 - leakage assessment & shielding effectiveness, weekly report presented 7/29
Week 2 (8/4-8/12): Node 4/5
- Fixed a unit bug that invalidated earlier scans
- Converged the shield-radius design scan (leakage suppression)
- Node-5 analyses: rotational quadrupole, max reachable field, edge effects (2D->2.5D)
- Extended the shield-radius optimization to dipole mode (today)
- Started the English LaTeX design report

## Slide 3
Week 1 - Leakage & Shielding (Node 3)
- Compared shield-current solutions: least-squares method vs induced-current model
- chi2 parameter scans over design parameters
- Dipole shield-leakage analysis
- Leakage with / without shield, linear and log-log views
- Shield-current distribution vs shield gap
- Deliverable: weekly_report.pptx (presented at 7/29 meeting)

## Slide 4
Week 2 (8/9) - Progress Check vs Summer Plan
Gaps identified:
- Pulse / material parameters not yet validated
- Node-4 optimal-design scan had not converged
- No technical notes yet
Scope decisions:
- Induced eddy-current model and field3d excluded from the report
- 2D-only technical note: 8-chapter outline drafted
- Started sweeping shield radius (influence on shielding)

## Slide 5
Week 2 (8/11) - Unit Bug Fix + Shield Radius Sweep
- Fixed unit bug: ring_meanB returns T, not mT -> earlier scans redone
- Swept shield radius 25-79 mm at 1 mT/mm target, 1000 A budget
- Leakage rises monotonically with shield radius
- Optimum: R_sh ~ 27 mm (default 27.5 mm is near-optimal)
- Figure: figures/shield_radius_optimization.png

## Slide 6
Node 5 - Rotational Quadrupole
Field-current map is exactly linear, geometry is fixed -> rotated quadrupole needs only a current combination:
- I(phi) = cos(2*phi) * I_normal + sin(2*phi) * I_skew
- Verified against a full re-solve at every angle (residual ~ solver round-off)
- Practical result: rolling the field requires no new solve - two fixed current patterns suffice

## Slide 7
Node 5 - Max Reachable Field & Edge Effects
Max reachable central field (coils capped at 1000 A):
- Hardware ceiling via linear programming: I_k = I_max * sign(n.c_k)
- Achievable field under field-quality constraints (least-squares design)
Edge effects (2D -> 2.5D, finite coil length L):
- Exact mid-plane correction factor per wire: f(rho; L) = [1 + (2*rho/L)^2]^(-1/2)
- Quantifies how far the infinite-wire 2D model can be trusted

## Slide 8
Today (8/12) - Shield Radius Optimization in Dipole Mode
- Parameterized optimize_shield_radius.py with solve_dipole_coils
- Scan result (fixed central target, 1000 A coil budget):
* Quadrupole (1 mT/mm): optimum R_sh = 27 mm, required current ~ 886 A
* Dipole (1 mT): optimum R_sh = 25 mm, required current ~ 222 A
- Required current decreases strictly monotonically with R
- A single shield radius serves both field modes
Quadrupole scan
Dipole scan

## Slide 9
Today (8/12) - Reframed Optimization (Hardware-Fixed)
- New framing: fix I_coil = 1000 A (hardware cap), find the minimum shield radius that still meets the target field
- Exact roots of I_coil(R) = 1000 A:
* Quadrupole: R_sh = 26.233 mm
* Dipole: R_sh = 22.99 mm
- The dipole root sits only 0.49 mm outside the coil ring (22.5 mm) -> mechanically infeasible
- Practical dipole minimum: 23.5-24 mm

## Slide 10
Conclusion - Single Shield Design
- Quadrupole mode drives the shield radius: R_sh ~ 27 mm (>= 26.233 mm) satisfies both modes
- Dipole alone could use a smaller shield (>= 23.5-24 mm), but gains nothing - the quadrupole requirement dominates
- Dipole is far less demanding on current: 222 A vs 886 A -> ample headroom under the 1000 A cap
- Recommendation: single shield at R_sh ~ 27 mm

## Slide 11
Status vs Plan & Next Steps
Node 5 (today) content complete:
- Rotational quadrupole
- Max reachable field
- Edge effects
Technical note:
- 8-chapter outline drafted (2D only); English LaTeX report started
Next:
- Node 6 (8/19): full dry-run, technical note near-final
- Node 7 (8/20): final oral report + technical note (deadline)